## Slide 1
PlastiBytes
Bottles in. A 3D pen out.
FlowForge is a handheld 3D printing pen made from a dead 3D printer, running on filament made from drink bottles.
Makers, open hardware community, exhibition visitors · August 2026 · PlastiBytes
Notes: Open by holding the pen up before saying anything.,One line: the machine is waste, the plastic is waste, the body is printed from the same plastic.,Say where you are building it: Yaounde, Cameroon.

## Slide 2
THE PROBLEM
Every maker space sits on two piles of waste that never meet: dead 3D printers and empty PET bottles.
A printer is usually retired for one failure. The hot end, the steppers and the extruder gears are still perfect.
2
Notes: Name the single failure that kills a printer: warped bed, fried board, seized lead screw.,The expensive parts survive the machine.,PET bottles are chemically close to the PETG makers pay import prices for.

## Slide 3
WHY IT IS STUCK
A commercial 3D pen is a closed box, and imported filament is priced for somewhere else
You cannot open it
No schematics, no spares. A clogged nozzle turns the pen into waste.
You cannot change it
Temperature and speed are fixed by the maker.
The filament is imported
Every spool arrives by ship, priced in a foreign currency.
3
Notes: Keep this short. It is the setup, not the argument.,Expect: 'why not just buy a pen?' Answer: you can, once, and then you own a sealed object.,Do not quote a filament price here, the local figure is still being measured.

## Slide 4
THE IDEA
FlowForge is built from a dead printer, fed on bottle plastic, and wrapped in a body printed from that same plastic.
A FlowForge can print the parts for the next FlowForge. That is what makes it a loop and not a gesture.
4
Notes: This is the slide the whole talk hangs on. Slow down.,Three axes recovered at once: machine, feedstock, enclosure.,As far as we can establish, no other open pen closes all three.

## Slide 5
WHAT IT IS MADE OF
Almost nothing in this pen was bought new
9 of 11
line items on the bill of materials are salvaged
0
new microcontrollers, sensors or motors bought
74 g
recycled PET printed into the enclosure
Source: FlowForge build documentation, section 3
5
Notes: Only fasteners, wiring and the bench supply are new.,The 74 g is the seven printed parts, 73.97 g measured in the slicer.,Expect: 'is this reproducible without a donor printer?' Yes, the BOM lists a new equivalent for every part.

## Slide 6
HOW IT WORKS
The heavy half stays on the desk. The hand holds 40 g, not 400 g
24 V bench supply feeds a desktop electronics wedge
Arduino Mega and RAMPS 1.6, both pulled from the donor printer
Salvaged NEMA 17 pushes filament down a PTFE tether
The pen carries only the hot end, thermistor and fan
PHOTO
The electronics wedge and the pen on a bench, tether connecting them, filament spool visible at the rear inlet, natural daylight
6
Notes: The tether is a trade we made on purpose, not a compromise we are hiding.,It also keeps stepper heat and vibration away from the grip.,Expect: 'why such a big board?' Because it is the donor printer's own board. Zero new silicon.

## Slide 7
THE PEN
The barrel is ribbed because the heat has to go somewhere
PHOTO
Close-up of the pen barrel and hot end vent, held in hand, shallow depth of field, grey rPET surface texture visible
No printed plastic touches the heat break. The wall stands off with an air gap.
7
Notes: The ribs are cooling surface, not styling.,Heat break is 11.9 mm across and 5.7 mm long, the critical dimension in the whole design.,rPET would soften long before the hot end reaches working temperature.

## Slide 8
PRINT IT YOURSELF
Seven printed parts, and the two frame bodies are most of the print
Chart: 
| Top frame | Bottom frame | Top body | Knob | Badge | Support | Screen trim
grams of rPET | 41.71 | 27.54 | 1.37 | 1.23 | 0.9 | 0.79 | 0.43
73.97 g of recycled PET, about 7,400 XAF (~$12) of material, and the two frame bodies are 94 percent of it.
Source: FlowForge print schedule, section 5
8
Notes: Print the frames first, the small parts are quick reprints if you revise.,Material cost is at roughly 100 XAF per gram of recycled filament.,STL files are in the repository.

## Slide 9
SAFETY
A 260 degree heater in a hand-held object gets three independent ways to shut itself down
Sensor sanity band
A reading below 5 or above 300 degrees means the thermistor is wrong. Heater off.
Hard ceiling
260 degrees is the ceiling. Past it the heater cuts and the fault latches.
Runaway watchdog
Heating hard for 20 seconds without climbing means something is broken.
9
Notes: This is the most important code in the project. Say so.,A disconnected thermistor reads at the rail. That is the classic path to a fire, and the sanity band catches it.,Any fault kills the heater, disables the extruder, runs the fan flat out and latches until power cycle.

## Slide 10
HONEST PART
Bottle PET is not a drop-in filament, and we are not going to pretend it is
It drinks water out of the air
Dry at 65 degrees, 4 hours minimum. Wet again within hours.
Diameter wanders
Strip-cut filament inherits every wobble in the bottle wall.
It is stiffer than PETG
Bottle PET crystallises more, so it snaps in the guide tube.
The fix is process
Wash, dry, draw, dry again, gauge before loading.
10
Notes: Do not skip this slide to look good. It is the part makers trust.,Glue residue from labels chars in the melt zone and is a common clog.,Failure-mode table is in the documentation, section 8.

## Slide 11
ROADMAP
Where FlowForge goes next
1
V1, now
Tethered pen, salvaged Mega and RAMPS, build files published
2
V2
Untethered on a Xiao ESP32-C3, controller moves into the hand
3
Feedstock
Bottle to filament brought in-house so the loop closes under one roof
4
Reliability
Filament diameter sensor with live flow compensation
11
Notes: The diameter sensor is the single change that would most improve rPET reliability.,V2 cuts the tether down to filament only.,A desktop app for per-batch temperature profiles is also on the list.

## Slide 12
YOUR TURN
Take the files and build one.
Hardware under CERN-OHL-S v2, firmware under MIT. STLs, wiring, pin map and the full build guide are open. Tell us what breaks.
www.plastibytes.com · info@plastibytes.com
Bridging Africa's innovation gap while tackling plastic pollution, one recycled bottle at a time.
PlastiBytes
12
Notes: Ask for one thing: a build attempt and a report back.,Point at the repository and the documentation.,If someone has a dead printer, that is the conversation to have after.